## Slide 1: CASSIA Scales
Software Operation Description.

## Slide 2: STARTUP PROCESS
Initialise hardware registers:
  A/D
  Serial
  I2C
  I/O ports.
Read Settings from EEPROM.

## Slide 3: STARTUP CONDITIONS
Local = TRUE
Factory = FALSE
unit = if defined (from EEPROM) else grams
zeroVal = if defined (from EEPROM) else 0.
numberOfSamples = if defined (from EEPROM) else default (8).
Calibration values = if defined (from EEPROM) else default.
Asks user to select Local or Remote operation mode.

## Slide 4: USER_LOCAL
Selectable at startup and from USER_REMOTE menu.
Local = TRUE
Input via Keypad, PICDEM 2 Plus onboard hardware.
Output via LCD, LEDs and Voice synth board.

## Slide 5: USER_REMOTE
Selectable at startup and from USER_LOCAL menu.
Local = FALSE
Input via: RS232 though HyperTerminal or proprietary Terminal Emulator.
Output via: RS232 though HyperTerminal or proprietary Terminal Emulator.

## Slide 6: MUTE
Disables output via speech synth chip.
Mute = TRUE
Write to EEPROM.

## Slide 7: SET_MODE_WEIGH
The default mode of the system.
The system will constantly take weight samples and fill a circular buffer.
The buffer is averaged and the zero value is subtracted.
The average is divided by the value used for grams, ounces or user defined units.
The output is displayed via the active display method. This Displays weight as #### <units>

## Slide 8: SET_MODE_COUNT
When called, SET_MODE_COUNT will ask if the user wants to define a new unit or skip (recall old unit).
If yes, asks how many of said unit are currently in the basket?
Divide raw weight average by num to get custom user unit value.
Return to SET_MODE_WEIGH function using new unit.

## Slide 9: TARE
The zero value is updated with the average raw weight.
Write to EEPROM

## Slide 10: SET_WEIGHT_GRAMS
Divisor value updated to value for grams
Unit type is updated to ‘grams’
Write to EEPROM

## Slide 11: SET_WEIGHT_OUNCES
Divisor value updated to value for ounces
Unit type is updated to ‘ounces’
Write to EEPROM

## Slide 12: SET_MODE_FACTORY
Enter by holding 1 and 9 on keypad and typing ‘admin’ during remote mode.
Sets boolean value ‘factory’ to TRUE allowing calls to:
  CALIBRATE
  SET_SAMPLES_PER MEASUREMENT
  SHOW_WEIGHT_READINGS
  SHOW_STATISTICS
  SET_MODE_USER
Sets boolean value ‘local’ to FALSE.

## Slide 13: CALIBRATE
Enters calibration mode.
O hai, I can has kalibrashun?
Write calibration model to EEPROM.
On complete, return.

## Slide 14: SET_SAMPLES_PER_MEASUREMENT
Asks for a new number of samples.
Updates size of used weight measurements buffer.
Write to EEPROM.

## Slide 15: SHOW_WEIGHT_READINGS
Shows current raw reading.
Waits for keypress to return.

## Slide 16: SHOW_STATISTICS
Displays to HyperTerminal required statistics.
Oh Hai, I can has required statistics?
Waits for keypress to return.

## Slide 17: SET_MODE_USER
Sets boolean value ‘factory’ to FALSE